FCAW: Terms & Defects: Part 1 of 2 (WDTM18) The learner will demonstrate knowledge of flux cored arc welding terminology and defects. Author - David Crawford

Question 1: If the electrode wire is rusty on the spool, ______________ may result. Answer 1: porosity Answer 2: fusion Answer 3: penetration Answer 4: slag inclusions Correct Answer: porosity

Question 2: Excessive electrode extension requires an increase in what to adequately blanket the weld pool: Answer 1: voltage Answer 2: amperage Answer 3: wire feed speed Answer 4: shielding gas Correct Answer: shielding gas

Question 3: To reduce surface tension, the mill scale could be ground off or the use of ____________ also helps. Answer 1: increased voltage Answer 2: argon shielding gas Answer 3: increased amperage Answer 4: forehand welding Correct Answer: argon shielding gas

Question 4: Undercutting and an unstable arc are more problematic with which type of shielding gas? Answer 1: Mixed Argon/CO﻿2 Answer 2: 100% Carbon Dioxide Answer 3: Argon/Helium Answer 4: 100% Nitrogen Correct Answer: 100% Carbon Dioxide

Question 5: Porosity in a straight line is called aligned porosity. What is it called if the porosity is all over the weld? Answer 1: Random Porosity Answer 2: Non-Linear Porosity Answer 3: Scattered Porosity Answer 4: Dirty Porosity Correct Answer: Scattered Porosity

Question 6: A crack at the end of the weld is called a: Answer 1: end crack Answer 2: weld crack Answer 3: stranded crack Answer 4: crater crack Correct Answer: crater crack

Question 7: With an improper work angle you will likely end up with ______________ or incomplete penetration. Answer 1: incomplete fusion Answer 2: incomplete undercut Answer 3: insufficient penetration Answer 4: carbide precipitation Correct Answer: incomplete fusion

Question 8: Two similar types of incomplete fusion to the base metal are called cold lap and ______________. Answer 1: underfill Answer 2: burn through Answer 3: overlap Answer 4: cracking Correct Answer: overlap

Question 9: An unacceptable flaw is called a _______________. Answer 1: detection Answer 2: failure Answer 3: discontinuity Answer 4: defect Correct Answer: defect

Question 10: Round scattered droplets of weld metal that are unsightly and may lead to stress riser cracking is: Answer 1: underfill Answer 2: spatter Answer 3: overlap Answer 4: cold lap Correct Answer: spatter

Question 11: If the base metal at the toes of the weld are melted away, the defects or discontinuities are called ______________. Answer 1: underfill Answer 2: undercut Answer 3: burn through Answer 4: melt through Correct Answer: undercut

Question 12: Identify what "A" represents. Answer 1: Stick-Out Answer 2: Stand-Off Answer 3: Electrode Extension Answer 4: Arc Length Correct Answer: Stand-Off

Question 13: Identify what "B" represents. Answer 1: Arc Length Answer 2: Stick-Out Answer 3: Electrode Extension Answer 4: Stand-Off Correct Answer: Electrode Extension

Question 14: Identify what "C" represents. Answer 1: Stand-Off Answer 2: Electrode Extension Answer 3: Stick-Out Answer 4: Arc Length Correct Answer: Stick-Out

Question 15: Identify what "D" represents. Answer 1: Arc Length Answer 2: Stand-Off Answer 3: Stick-Out Answer 4: Electrode Extension Correct Answer: Arc Length

GAMMA+ by Fox Valley Technical College is licensed under a Creative Commons Attribution 3.0 Unported License.

This workforce product was funded by a grant awarded by the U.S. Department of Labor’s Employment and Training Administration. The product was created by the grantee and does not necessarily reflect the official position of the U.S. Department of Labor. The U.S. Department of Labor makes no guarantees, warranties, or assurances of any kind, express or implied, with respect to such information, including, but not limited to, accuracy of information or its completeness, timeliness, usefulness, adequacy, continued availability, or ownership. Auxiliary aids and services are available upon request to individuals with disabilities. This equal opportunity program is part of a grant from the U.S. Department of Labor equaling $2,999,750.00.